INITIAL WRITTEN ASSESSMENT for Modification Proposal P203 ‘Introduction of a Seasonal Zonal Transmission Losses Scheme’

Prepared by:  ELEXON Limited

| Date of Issue: | 7 July 2006 | Document Reference: | P203IR |
| --- | --- | --- | --- |
| Reason for Issue: | For Panel decision | Version Number: | 1.0 |

This document has been distributed in accordance with Section F2.1.10 of the Balancing and Settlement Code.

P203 seeks to introduce an annual calculation of seasonal Transmission Loss Factor (TLF) values (one per BSC Season for each TLF Zone) which is identical to Alternative Modification P198, except that (unlike P198 Alternative) there would be no phased implementation of these values. BSCCO’S RECOMMENDATIONS On the basis of the initial assessment BSCCo recommends that the Panel: DETERMINE that Modification Proposal P203 should be submitted to the Assessment Procedure; AGREE the Assessment Procedure timetable such that an Assessment Report should be completed and submitted to the Panel for consideration at its meeting of 10 August 2006; DETERMINE that the P203 Modification Group be formed from members of the P198 and P200 Modification Groups; and AGREE the Modification Group Terms of Reference.

CONTENTS TABLE

Summary of Impacted Parties and Documents	3

1	Description of Proposed Modification	4

1.1	Background	4

1.2	Related Modification Proposals	5

1.3	Modification Proposal P203	10

1.4	Areas for Consideration in Progressing Modification Proposal	10

2	Rationale for BSCCo’s Recommendations to the Panel	13

3	Terms Used in this Document	14

4	Document Control	14

4.1	Authorities	14

4.2	References	14

4.3	Intellectual Property Rights, Copyright and Disclaimer	14

Appendix 1: Modification Proposal	15

Appendix 2: Initial Assessment of Impacts of Modification Proposal	19

Appendix 3: Costs and Timetable for Progression	24

Summary of Impacted Parties and Documents

As far as BSCCo has been able to assess, the following parties/documents are potentially impacted by Modification Proposal P203.

Please note that this table represents a summary of the full initial impact assessment results contained in Appendix 2.

| Parties | Sections of the BSC | Code Subsidiary Documents |
| --- | --- | --- |
| Distribution System Operators |  | A |  | BSC Procedures |  |
| Generators |  | B |  | Codes of Practice |  |
| Interconnectors |  | C |  | BSC Service Descriptions |  |
| Licence Exemptable Generators |  | D |  | Party Service Lines |  |
| Non-Physical Traders |  | E |  | Data Catalogues |  |
| Suppliers |  | F |  | Communication Requirements Documents |  |
| Transmission Company |  | G |  | Reporting Catalogue |  |
| Party Agents |  | H |  | Load Flow Model Specification* |  |
| Data Aggregators |  | I |  | Core Industry Documents |
| Data Collectors |  | J |  | Ancillary Services Agreement |  |
| Meter Administrators |  | K |  | British Grid Systems Agreement |  |
| Meter Operator Agents |  | L |  | Data Transfer Services Agreement |  |
| ECVNA |  | M |  | Distribution Codes |  |
| MVRNA |  | N |  | Distribution Connection Agreements |  |
| BSC Agents | O |  | Distribution Use of System Agreements |  |
| SAA |  | P |  | Grid Code |  |
| FAA |  | Q |  | Master Registration Agreement |  |
| BMRA |  | R |  | Supplemental Agreements |  |
| ECVAA |  | S |  | Use of Interconnector Agreement |  |
| CDCA |  | T |  | BSCCo |
| TAA |  | U |  | Internal Working Procedures |  |
| CRA |  | V |  | BSC Panel/Panel Committees |
| SVAA |  | W |  | Working Practices |  |
| Teleswitch Agent |  | X |  | Other |
| BSC Auditor |  |  | Market Index Data Provider |  |
| Profile Administrator |  |  | Market Index Definition Statement |  |
| Certification Agent |  |  | System Operator-Transmission Owner Code |  |
| Transmission Loss Factor Agent* |  |  | Transmission Licence |  |
| Other Agents |  | Network Mapping Statement* |  |
| Supplier Meter Registration Agent |  |  | Load Flow Model Reviewer* |  |
| Data Transfer Service Provider |  |  |  |

Description of Proposed Modification

Background

    - Types of Transmission Losses

The total metered energy which can be drawn from the Transmission System to meet demand will always be less than that delivered onto the Transmission System by generation, since some energy is used up in the process of transporting electricity.  The energy ‘lost’ from the Transmission System is commonly referred to as ‘transmission losses’.  Transmission losses can be considered to comprise two main elements:  ‘fixed’ losses and ‘variable’ losses.

Fixed losses are those which do not vary significantly with the power flow.  In transformers, the losses arise from magnetising the iron core.  In overhead lines, they include losses dependent on the voltage levels, length of line and climatic conditions.

Variable losses arise through the heat caused by current flowing through the transformers and lines.  Variable losses increase with the current (and associated power flow) and the length of line in which it flows.

References to ‘fixed’ and ‘variable’ losses throughout this document have the meaning given above, whilst the term ‘total’ transmission losses is used to represent the sum of fixed and variable losses (i.e. the total energy lost from the Transmission System at any given point in time, calculated as the difference between total generation and demand).

    - Existing Allocation Mechanism for Transmission Losses

The rules and calculations for allocating transmission losses to Parties are set out in Section T2 of the Balancing and Settlement Code (‘the Code’).  These involve the adjustment of individual BM Unit Metered Volumes in Settlement to allocate transmission losses, whilst ensuring that total adjusted generation matches total adjusted demand in any given Settlement Period.  Transmission losses are thereby allocated to Parties as part of their Trading Charges.

Under the existing Code provisions, both fixed and variable transmission losses in each Settlement Period are allocated to Parties on a ‘uniform’ (non-locational) basis in proportion to each Party’s metered energy.  The current allocation of transmission losses therefore does not take account of the extent to which individual Parties give rise to such losses.  Although a parameter for a ‘differential’ allocation of some or all transmission losses is included in the Code, this is currently set to zero so has no practical effect.  In the Section T calculation, this parameter is represented by the Transmission Loss Factor (TLF=0).  This value can only be amended through a modification to the Code.

The formula below represents a simplified version of the Section T calculation for each BM Unit’s share of total transmission losses in any given Settlement Period:

TLM=1+TLF+TLMO

A Transmission Loss Multiplier (TLM) is generated for each individual BM Unit, and represents a factor used to scale the BM Unit’s Metered Volumes in Settlement.  The purpose of the Transmission Losses Adjustment (TLMO) is to uniformly adjust all generation delivery and all demand offtake, in order to allocate the proportion of transmission losses which has not already been allocated through the TLF.  Metered Volumes for BM Units in ‘delivering’ (exporting) Trading Units are multiplied by 1+TLF+TLMO+ (with TLF=0 this is a scaling down), whilst Metered Volumes for BM Units in ‘offtaking’ (importing) Trading Units are multiplied by 1+TLF+TLMO- (with TLF=0 this is a scaling up).

The value of TLMO+/- is produced by a separate calculation in Section T.  This includes the application of an ‘alpha (() factor’ of 0.45, which uniformly adjusts the total transmission losses for the Settlement Period such that 45% of losses are allocated across all delivering Trading Units in aggregate whilst 55% are allocated across all offtaking Trading Units in aggregate.

The formulae below represent simplified versions of the TLMO+ and TLMO- calculations:

TLMO+ = -(0.45*(total transmission losses in Settlement Period) – generators’ share of transmission losses already allocated through TLF in Settlement Period) / total volume of generation in Settlement Period

TLMO- = (0.55*(total transmission losses in Settlement Period) – Suppliers’ share of transmission losses already allocated through TLF in Settlement Period) / total volume of demand in Settlement Period

The value of TLMO+ is the same in each Settlement Period for every BM Unit in all delivering Trading Units.  The value of TLMO- is the same for every BM Unit in all offtaking Trading Units.

Since under the existing Code baseline the value of TLF is set to zero, the TLMO is currently the only determining factor in the calculation of each BM Unit’s TLM.  Two uniform TLM values are therefore currently applied:  one to all BM Units in delivering Trading Units, and one to all BM Units in offtaking Trading Units.  Each Party’s overall allocation of transmission losses is dependent on the Metered Volumes of the BM Units to which this TLM is applied.

  - Related Modification Proposals

There are currently three other Pending Modification Proposals being progressed in the area of zonal transmission losses, as follows:

- Modification Proposal P198 ‘Introduction of a Zonal Transmission Losses Scheme’ (raised by RWE Npower on 16 December 2005);

- Modification Proposal P200 ‘Introduction of a Zonal Transmission Losses Scheme with Transitional Scheme’ (raised by Teesside Power Limited on 21 April 2006); and

- Modification Proposal P204 ‘Scaled Zonal Transmission Losses’ (raised by British Energy Power & Energy Trading Ltd on 3 July 2006).

In addition, the P198 and P200 Modification Groups have developed Alternative Modifications for both P198 and P200.  All of the proposals seek to introduce a locational allocation of variable losses through the calculation of ‘zonal’ TLF values, although their precise calculations and application of these values differ.  A summary of the solutions can be found in Table 1 on the following page, whilst further detail regarding the proposals and their Alternatives can be found in Sections 1.2.1-1.2.4 below.

Please note that all three of these Modification Proposals and their Alternatives are mutually exclusive, such that only one could be approved by the Authority for implementation.

Table 1 – Summary of Transmission Losses Modification Proposals

The key aspects of Modification Proposals P198, P200 and P204 are outlined below, and are shown against the P203 solution for comparison.

| Aspect of Solution | P198 Proposed | P198 Alternative | P200 Proposed | P200 Alternative | P203 Proposed | P204 Proposed |
| --- | --- | --- | --- | --- | --- | --- |
| Scope of Zonal TLF Calculation | Scaled Marginal (Variable Losses Only) | Scaled Marginal (Variable Losses Only) | Scaled Marginal (Variable Losses Only) | Scaled Marginal (Variable Losses Only) | Scaled Marginal (Variable Losses Only) | Scaled Marginal (Variable Losses Only) |
| Scaling Factor | 0.5 (Single Scaling Factor Fixed in Code) | 0.5 (Single Scaling Factor Fixed in Code) | 0.5 (Single Scaling Factor Fixed in Code) | 0.5 (Single Scaling Factor Fixed in Code) | 0.5 (Single Scaling Factor Fixed in Code) | TBC, with 2 Options: Option 1 – Single Scaling Factor; or Option 2 – Different Scaling Factor Calculated and Applied in each Settlement Period |
| Aim of Scaling Factor | Ensure Total Variable Losses Allocated Through TLFs | Ensure Total Variable Losses Allocated Through TLFs | Ensure Total Variable Losses Allocated Through TLFs | Ensure Total Variable Losses Allocated Through TLFs | Ensure Total Variable Losses Allocated Through TLFs | Ensure No BM Units are Credited with Energy Through TLM |
| Applicable Period for TLFs | BSC Year | BSC Season | BSC Year | BSC Season | BSC Season | BSC Year |
| Nature of TLF Calculation | Ex-Ante | Ex-Ante | Ex-Ante | Ex-Ante | Ex-Ante | Ex-Ante |
| Frequency of TLF Calculation | Annual | Annual | Annual | Annual | Annual | Annual |
| Applicable Zones for Production BM Units | GSP Group | GSP Group | GSP Group | GSP Group | GSP Group | GSP Group |
| Applicable Zones for Consumption BM Units | GSP Group | GSP Group | GSP Group | GSP Group | GSP Group | GSP Group |
| Mitigation of Impacts? | No | Yes | Yes | Yes | No | No |
| Type of Mitigation | - | Linear Phasing | Hedging | Hedging | - | - |
| Period of Mitigation | - | 4 Years | 15 Years | 15 Years | - | - |

    - Modification Proposal P198

P198 is currently part-way through the Assessment Procedure, with an Assessment Report to be presented to the BSC Panel (‘the Panel’) at its meeting on 10 August 2006.

- Proposed Modification P198

The solution for Proposed Modification P198 involves the following ‘scaled marginal’ methodology for calculating zonal TLFs:

- An electrical model of the Transmission System (a ‘Load Flow Model’) would be built, containing ‘Nodes’ to represent points where energy flows on or off the Transmission System.  Each Node on the Transmission System would be identified by the Transmission Company, and would be allocated to a specific Zone on the transmission network on the basis of a ‘Network Mapping Statement’ maintained by BSCCo.  The TLF Zones would be set by the Panel, based on the geographic areas covered by GSP Groups.  Since there are currently 14 GSP Groups, there would therefore be 14 TLF Zones.

- TLFs would be calculated on an ex-ante basis (i.e. forecasted) for each BSC Year, using Metered Volumes and Network Data for Sample Settlement Periods from a preceding 12-month period (the ‘Reference Year’).  The required Metered Volumes and Network Data would be provided by the Central Data Collection Agent (CDCA) and the Transmission Company respectively.

- Prior to the start of each BSC Year (1 April – 31 March), the Load Flow Model would be run by a Transmission Loss Factor Agent (‘the TLFA’) to calculate how an incremental (or ‘marginal’) increase (or ‘injection’) in power at each individual Node would affect the total variable losses from the Transmission System.  The output of the Load Flow Model would be a TLF value for each Node in each of the Sample Settlement Periods.   Positive TLF values would be produced for Nodes where an incremental increase in generation (or reduction in demand) had the effect of decreasing variable losses.  Negative TLF values would be produced for Nodes where an incremental increase in generation (or reduction in demand) had the effect of increasing variable losses.  For example, if an injection of an extra 1kWh of energy at a Node increased variable losses by 0.02 kWh, the TLF for that Node in that Settlement Period would be -0.02.

- The TLFA would average these raw Nodal TLFs across all the Nodes in each TLF Zone by ‘volume-weighted’ averaging, to give 14 Zonal TLF values for each Sample Settlement Period (one per TLF Zone).  The TLFA would then convert these to Annual Zonal TLFs by ‘time-weighted’ averaging.

- The TLFA would adjust the Annual Zonal TLFs by a 0.5 scaling factor such that the volume of energy allocated via the TLFs was comparable to the volume of variable losses calculated by the Load Flow Model.  These 14 Adjusted Annual Zonal TLFs (one per TLF Zone) would be made publicly available by BSCCo no less than three months prior to their use in the TLM Settlement calculation for the applicable BSC Year.

- Each BM Unit would be allocated to a specific TLF Zone by BSCCo on the basis of the Network Mapping Statement, with any question or dispute over their zonal allocation to be resolved by the Panel.  Using the Network Mapping Statement, the TLFA would determine the TLF value to be applied to each BM Unit in the TLM Settlement calculation for the applicable BSC Year.  This BM Unit-Specific TLF would be the Adjusted Annual Zonal TLF value for the Zone in which the BM Unit was located. All BM Units within a Zone would therefore receive the same single TLF value (the Adjusted Annual Zonal TLF for that Zone), for every Settlement Period within the applicable BSC Year.  A positive TLF value would increase the value of TLM used to scale a BM Unit’s Metered Volume (a benefit to generators and disadvantage to Suppliers), whilst a negative TLF value would decrease the value of TLM (a benefit to Suppliers and disadvantage to generators).

- The BM Unit-Specific TLFs calculated by the TLFA would be registered in BSC Systems by the Central Registration Agent (CRA), and would be used by the Balancing Mechanism Reporting Agent (BMRA) and the Settlement Administration Agent within the Balancing Mechanism Reporting Service (BMRS) and Settlement calculations respectively.

- The remaining ‘fixed’ element of transmission losses would continue to be allocated to Parties on a non-locational basis through the TLMO, and the overall 45:55 allocation of total transmission losses to generation and demand would be retained.

- There would be no phased implementation or ‘hedging’ of exposure to the new zonal TLFs, which would therefore take full effect from the first Settlement Period on the Implementation Date.

Further detail regarding Proposed Modification P198 can be found in the P198 Second Assessment Procedure Consultation Document (Reference 1).

- Alternative Modification P198

Under Alternative Modification P198, the TLFA would calculate Nodal TLFs and Zonal TLFs in the same way as for Proposed Modification P198, but would time-weight by BSC Season rather than by BSC Year to calculate a set of four Seasonal Zonal TLFs for each TLF Zone – one for each BSC Season.

The BSC Seasons are already defined in Section K of the Code, and are:

BSC Spring:	1 March – 31 May inclusive;

BSC Summer:	1 June – 31 August inclusive;

BSC Autumn:	1 September – 30 November inclusive; and

BSC Winter:	1 December – 28 February inclusive (or 29 February in a leap year).

These Seasonal Zonal TLFs would be multiplied under the same 0.5 scaling factor as under the Proposed Modification to ensure that the level of variable losses allocated through these TLFs was comparable to that calculated by the Load Flow Model.  However, under the Alternative Modification, the Seasonal Zonal TLFs would also be multiplied by an additional ‘beta’ (() scaling factor to create the final set of four Adjusted Seasonal Zonal TLFs.

The value of the ( scaling factor would be as follows:

Applicable BSC Year 1:			0.20

Applicable BSC Year 2:			0.40

Applicable BSC Year 3:			0.60

Applicable BSC Year 4:			0.80

Applicable BSC Year 5 onwards:		1.

Adjusted Seasonal Zonal TLF values would therefore be phased in linearly over the first four BSC Years of the scheme, such that they were applied at 20% of their full value in BSC Year 1, 40% in BSC Year 2, 60% in BSC Year 3, 80% in BSC Year 4, and 100% in BSC Year 5 and all subsequent years.  This scaling would be undertaken by the TLFA as part of its annual ex-ante calculation of TLFs.

All BM Units within a Zone would receive the Adjusted Seasonal Zonal TLF value for that Zone in the applicable season.   TLFs would be recalculated for each BSC Year, based on data from a previous Reference Year.

Since the BSC Spring season (1 March – 31 June) spans the beginning of a new BSC Year on 1 April, the new set of TLFs for each year would therefore come into effect part-way through this season.  This would result in a changeover from the BSC Spring seasonal TLF value applied to a BM Unit on the last Settlement Period on 31 March to a new value for that season which was effective from the first Settlement Period on 1 April.

Further detail regarding Alternative Modification P198 can be found in the P198 Second Assessment Procedure Consultation Document.

    - Modification Proposal P200

P200 is currently part-way through the Assessment Procedure, with an Assessment Report to be presented to the Panel at its meeting on 10 August 2006.

- Proposed Modification P200

Proposed Modification P200 seeks to introduce zonal TLFs under the same methodology as Proposed Modification P198 (i.e. an annual ex-ante calculation of one Adjusted Annual Zonal TLF value per TLF Zone), but with the addition of an F-factor ‘hedging’ scheme to mitigate the impact of TLFs on existing generators over 15 years.

P200 had been considered as a potential option for an Alternative Modification to P198.  However, the P198 Modification Group agreed by majority not to assess a hedging scheme in favour of a linear phasing approach.  P200 was subsequently raised as a separate Modification Proposal.

Further detail regarding Proposed Modification P200 can be found in the P200 Assessment Procedure Consultation Document (Reference 2).

- Alternative Modification P200

Alternative Modification P200 seeks to introduce zonal TLFs under the same methodology as Alternative Modification P198 (i.e. an annual ex-ante calculation of four Adjusted Seasonal Zonal TLF values per TLF Zone), but with the addition of a 15-year F-factor ‘hedging’ scheme for existing generators.

Further detail regarding Alternative Modification P200 can be found in the P200 Assessment Procedure Consultation Document.

    - Modification Proposal P204

Like P198, Proposed Modification P204 seeks to introduce a zonal scheme for the allocation of variable losses, whereby annual TLF values would be calculated for each BSC Year on an ex-ante basis for each TLF Zone.  However, the principle behind P204 is different to P198, since it seeks to ensure that no BM Units are credited with energy (i.e. receive payments) through the TLM.

P204 had been considered as a potential option for an Alternative Modification to P198.  However, the Group agreed by majority not to further assess such an option further under P198 – believing either that it was outside the scope of P198, or that it required a substantive assessment in its own right and would be better assessed via a separate Modification Proposal.

The Initial Written Assessment (IWA) for P204 will be presented to the Panel at its meeting on 13 July 2006, with a recommendation that P204 be submitted to a three-month Assessment Procedure such that the P204 Assessment Report would be presented to the Panel at its meeting on 12 October 2006.

Further detail can be found in the P204 IWA (Reference 3).

Modification Proposal P203

P203 was raised on 26 June 2006 by RWE Npower (‘the Proposer’), who is also the Proposer of P198.  P203 seeks to introduce an annual calculation of seasonal TLF values which is identical to Alternative Modification P198, except that (unlike P198 Alternative) there would be no phased implementation of these values.

It should be noted that not all members of the P198 Modification Group who supported seasonal TLFs supported linear phasing, and vice versa.  The P198 Group noted that, under the BSC Modification Procedures, only one final Alternative Modification could be put forward to the Authority for decision – and that it was therefore not possible to develop seasonal TLFs and linear phasing as separate Alternatives.  The Group noted that including both options within one Alternative would involve the risk that such an Alternative might be rejected by the Authority, were the Authority to disagree with one of these elements.  The Group noted that this risk might be increased by the fact that some members in support of one of the elements did not necessarily support the other.  However, since there was a majority of members in favour of each element (although not necessarily in favour of both), the Group agreed by majority on 15 June 2006 that both seasonal TLFs and linear phasing should form the final Alternative Modification to P198.  P203 was subsequently raised as a separate Modification Proposal.

The Proposer of P203 believes that P203 would better facilitate the achievement of Applicable BSC Objectives (a), (b) and (c) for the same reasons as outlined in Modification Proposal P198 (i.e. removal of an existing cross-subsidy, providing signals for more economically efficient despatch and location of plant, reduction in the level of transmission losses).  Further detail regarding these arguments can be found in the P198 Second Assessment Procedure Consultation Document.

However, the Proposer believes that P203 would offer additional benefits over both Proposed Modification P198 and Alternative Modification P198 for the following reasons:

- On the basis of the external TLF modelling and cost-benefit analysis exercises carried out during the P198 Assessment Procedure, the Proposer believes that the use of seasonal TLF values would provide a more accurate allocation of losses than the use of annual values – leading to more efficient despatch and a greater reduction in the level of losses; and

- The exclusion of any phased or mitigated implementation of TLF values would avoid delaying the benefits associated with a zonal transmission losses scheme.

Areas for Consideration in Progressing Modification Proposal

An initial assessment of P203 has identified the following areas which BSCCo recommends should be considered further by a Modification Group during the progression of the Modification Proposal.

    - Solution and Assessment of Alternative Modification P198

a)  Solution

The Modification Proposal states that P203 would be based on the work already completed by the P198 Modification Group for Alternative Modification P198.  With the exception of its removal of the phasing element, the Modification Proposal therefore implies (though is not explicit) that all other elements of the solution for Proposed Modification P203 will be based on the solution already agreed by the P198 Group for Alternative Modification P198.  BSCCo therefore recommends that the Terms of Reference for the P203 Modification Group should state that the following areas of the solution for Proposed Modification P203 should mirror the requirements for Alternative Modification P198 as detailed in the P198 Second Assessment Procedure Consultation Document:

- Calculation of Nodal, Zonal, Seasonal Zonal, and Adjusted Seasonal Zonal TLF values (including the application of a 0.5 scaling factor which is fixed in the Code);

- Role of TLFA and Load Flow Model Reviewer;

- Access arrangements, input data, and output data for Load Flow Model;

- Basis for TLF Zones (the P203 Modification Proposal states that these will be based on GSP Groups for both generation and demand, consistent with P198);

- Duration (and start and end dates) of Reference Year;

- Requirements regarding the contents and maintenance of the Network Mapping Statement;

- Publication lead time for TLF values (set as three months under P198);

- Criteria for the retrospective recalculation of TLFs;

- Implementation approach (i.e. implementation and annual calculation tied to Parties’ contractual rounds); and

- Application of seasonal TLF values in Settlement (i.e. the use of a scripted approach to loading the TLF values into BSC Systems, with an annual changeover in the Spring TLF value on 1 April each year).

This approach would promote efficiency and the expeditious progression of P203, by avoiding the need to repeat discussions already undertaken by the P198 Group.  A longer progression timetable for P203 would be required if any of the above areas were to be revisited.

b)  Load-Flow Modelling

An external load-flow modelling exercise has been carried out by PTI Siemens on behalf of the P198 Modification Group.  This exercise included the calculation of unphased seasonal TLF values using 2005/6 data.  A copy of the full PTI modelling report can be found in the P198 Second Assessment Procedure Consultation Document.

On the assumption that (with the exception of the removal of the phasing element) the calculation of Adjusted Seasonal Zonal TLFs under Proposed Modification P203 would be the same as for Alternative Modification P198, no additional load-flow modelling would therefore be required for P203.

- Cost-Benefit Analysis

An external cost-benefit analysis of P198 was carried out by OXERA Consulting on behalf of the P198 Modification Group.  This analysis included a comparison between the net benefits of P198 which would arise from the use of both unphased annual and unphased seasonal TLF values.  A copy of the full OXERA cost-benefit analysis report can be found in the P198 Second Assessment Procedure Consultation Document.

On the assumption that (with the exception of the removal of the phasing element) the calculation of Adjusted Seasonal Zonal TLFs under Proposed Modification P203 would be the same as for Alternative Modification P198, no additional cost-benefit analysis would therefore be required for P203.

- Impact Assessment

During the P198 Assessment Procedure, separate impact assessments were sought from BSC Agents, Parties, BSCCo and the Transmission Company of the two elements of Alternative Modification P198 (seasonal TLF and linear phasing).  On the assumption that (with the exception of the removal of the phasing element) the calculation of Adjusted Seasonal Zonal TLFs under Proposed Modification P203 would be the same as for Alternative Modification P198, no additional impact assessment would therefore be required for Proposed Modification P203.

Respondents to the P198 Alternative impact assessment indicated that the costs of implementing only the seasonal element of the Alternative would be the same as implementing both the seasonal and phasing elements.  The costs of Proposed Modification P203 are therefore identical to those for Alternative Modification P198, as detailed in the P198 Second Assessment Procedure Consultation Document.

Please note, however, that if an Alternative Modification was to be developed for P203, a full impact assessment of that Alternative would be needed – requiring a longer progression timetable for P203.

    - Potential Options for an Alternative Modification

A standard part of a Modification Group’s assessment is to consider whether there may be any Alternative Modification which might better facilitate the achievement of the Applicable BSC Objectives when compared with the Proposed Modification.

The progression timetable set out in Section 2 of this IWA is based on the assumption that no Alternative Modification would be developed for P203.  The rationale for this assumption is that, of the variety of potential Alternative options considered under P198, only seasonal TLFs and linear phasing received majority support amongst the Group and have already been progressed as the final P198 Alternative.  Since the defects identified in, solutions proposed by, and issues associated with P198 and P203 are very similar, it is therefore unlikely that those options which had minority support and/or were believed to be outside the scope of P198 would be put forward under P203.  Further detail regarding the options considered under P198 can be found in the P198 Second Assessment Procedure Consultation Document.

BSCCo therefore recommends that the P203 Modification Group be mindful of the arguments expressed in respect of P198, in order to ensure consistency between the assessment of the two proposals.  However, should the Group wish to develop an Alternative Modification to P203, a longer progression timetable would be required.

    - Additional Activities for P203

Based on the assumptions that no Alternative Modification would be developed for P203, and that (with the exception of the removal of the phasing element) the solution for the Proposed Modification would be based on Alternative Modification P198, the only remaining progression activities for P203 would be:

- An industry consultation on the merits of P203 against the Applicable BSC Objectives; and

- The development of legal text.

BSCCo’s recommendation regarding the procedure and timescale for these activities can be found in Section 2.

Rationale for BSCCo’s Recommendations to the Panel

Section F of the Code states that the purpose of an Assessment Procedure is to:

“evaluate whether the Proposed Modification identified in a Modification Proposal better facilitates achievement of the Applicable BSC Objective(s) and whether any alternative modification would, as compared with the Proposed Modification, better facilitate achievement of the Applicable BSC Objective(s) in relation to the issue or defect identified in the Modification Proposal” (F2.6.2),

whilst new Modification Proposals will usually only be submitted directly to the Report Phase where:

“the Modification Proposal is of a minor or inconsequential nature and/or where the recommendation which the Panel should make to the Authority in relation to such Modification Proposal would generally be considered to be self-evident” (F2.2.5).

The arguments related to P203 are likely to be very similar to those expressed during the assessment of P198, and the results of the majority of the P198 assessment activities are also applicable to P203.  However, although the remaining progression activities for P203 (consultation and production of legal text) could potentially be carried out as part of a Report Phase, BSCCo believes that the recommendation to be made regarding P203 is not ‘self-evident’ for the following reasons:

- The industry consultation regarding the assessment of P198 has not yet concluded (the closing date for the consultation is 14 July 2006); and

- The P198 Modification Group has not yet agreed its final recommendation as to whether Proposed Modification P198 or Alternative Modification P198 should be made (the Assessment Report for P198 is due to be presented to the Panel on 10 August 2006).

BSCCo therefore recommends that P203 be submitted to the Assessment Procedure, with the P203 Modification Group to be formed from members of the P198 and P200 Modification Groups due to the related nature of these proposals (note that the membership of the P198 and P200 Groups is slightly different).

Based on the assumptions set out in Section 1.4, it is estimated that progression of P203 will require:

- 1 industry consultation (approximately 2 weeks’ duration);

- 2 Modification Group meetings (both to be potentially shared with P204, should the Panel agree the recommendations of the P204 IWA), in order to:

  - Agree a provisional recommendation as to whether P203 should be made, and the questions for the industry consultation (1 meeting); and

  - Consider the consultation responses and agree a final recommendation to the Panel (1 meeting), and

- Production of legal text (2 weeks’ duration, to be undertaken in parallel with the consultation).

Due to the similarities between P198 and P203, BSCCo is mindful of the desirability of submitting P203 to the Panel and the Authority in the same timescales as P198.  BSCCo believes that it would be possible to achieve the activities set out above within one month, such that the P203 Assessment Report was presented to the Panel on 10 August 2006 in parallel with the Assessment Reports for P198 and P200.

BSCCo therefore recommends that P203 be submitted to a one-month Assessment Procedure.  The proposed timetable and estimated costs for the progression of P203 are shown in Appendix 3.  BSCCo recommends that the areas for consideration raised by this IWA should form the basis of the Modification Group Terms of Reference, along with any additional areas proposed by the Panel.

The achievement of a one-month timetable is, however, dependent on the following assumptions:

- All elements of the solution for Proposed Modification P203 (other than removal of the phasing element) to be based on the solution already developed for Alternative Modification P198; and

- No Alternative Modification being developed for P203.

Should the Modification Group wish to undertake further work in these areas, an extension to this timetable would be required.

Terms Used in this Document

An explanation of all the terms used in this document can be found in the P198 Second Assessment Procedure Consultation Document.

Document Control

Authorities

| Version | Date | Author | Reviewer | Reason for Review |
| --- | --- | --- | --- | --- |
| 0.1 | 06/07/06 | Kathryn Coffin | Sarah Jones, Chris Rowell | For technical and quality review |
| 1.0 | 07/07/06 | Change Delivery |  | For Panel decision |

References

| Ref. | Document Title | Owner | Issue Date | Version |
| --- | --- | --- | --- | --- |
| 1 | Second Assessment Procedure Consultation Document for Modification Proposal P198 ‘Introduction of a Zonal Transmission Losses Scheme’ ELEXON - Modification Proposal 198 | BSCCo | 30/06/06 | 1.0 |
| 2 | Assessment Procedure Consultation Document for Modification Proposal P200 ‘Introduction of a Zonal Transmission Losses Scheme with Transitional Scheme’ ELEXON - Modification Proposal 200 | BSCCo | 30/06/06 | 1.0 |
| 3 | Initial Written Assessment for Modification Proposal P204 ‘Scaled Zonal Transmission Losses’ ELEXON - Modification Proposal 204 | BSCCo | 07/07/06 | 1.0 |

Intellectual Property Rights, Copyright and Disclaimer

This document contains materials the copyright and other intellectual property rights in which are vested in ELEXON Limited or which appear with the consent of the copyright owner.  These materials are made available for you to review and to copy for the purposes of your establishment or operation of or participation in electricity trading arrangements under the Balancing and Settlement Code (“BSC”).  All other commercial use is prohibited.  Unless you are a person having an interest in electricity trading under the BSC you are not permitted to view, download, modify, copy, distribute, transmit, store, reproduce or otherwise use, publish, licence, transfer, sell or create derivative works (in whatever format) from this document or any information obtained from this document otherwise than for personal academic or other non-commercial purposes.  All copyright and other proprietary notices contained in the original material must be retained on any copy that you make.  All other rights of the copyright owner not expressly dealt with above are reserved.

No representation, warranty or guarantee is made that the information provided is accurate, current or complete.  Whilst care is taken in the collection and provision of this information, ELEXON Limited will not be liable for any errors, omissions, misstatements or mistakes in any information or damages resulting from the use of this information or any decision made or action taken in reliance on this information.

Appendix 1: Modification Proposal

| Modification Proposal – BSCP40/06 | MP No: 203 (mandatory by BSCCo) |
| --- | --- |
| Title of Modification Proposal (mandatory by originator): Introduction of a seasonal Zonal Transmission Losses scheme |
| Submission Date (mandatory by originator): 26 June 2006 |
| Description of Proposed Modification (mandatory by originator) This modification is based on the seasonal alternative solution to P198 developed at the modification group but without any phasing. Seasonal zonal Transmission Loss Factors (TLF) (the “applicable TLFs”) would be derived ex ante for application to generation and demand BMUs within a zone (the “applicable zone”) for each of the four BSC seasons. The proposed scheme would retain the current process for allocating transmission losses to generation and demand (45% of transmission losses to production accounts and 55% to consumption accounts). Nodal marginal TLFs would be derived for each BMU from a representative collection of historic power system conditions using an intact network simulation (the “load flow model”) during a previous period (the “reference year”) that provided a representation of the settlement periods in each of the BSC seasons. The transmission company would provide appropriate data for the network simulation. BSCCo would provide a load flow specification for the load flow model. The calculation of the TLFs would be under the governance of the BSC. A TLF Agent or a service provider would undertake the load flow modelling. The modelling process and load flow model will be subject to independent review by the Panel and BSCCo. The applicable period for the seasonal zonal marginal TLFs under this proposal would be the BSC year (from April to March). Seasonal zonal marginal TLFs would be derived from nodal figures by volume-weighted averaging and time-weighted averaging for applicable zones. The applicable zones would be the geographical area in which a GSP Group lies, determined by the Panel (applying such criteria as it shall decide in its discretion). The zonal TLFs would be adjusted by an appropriate scaling factor (the “applicable scaling factor”, which was set at 0.5 under P82). The value of this scaling factor would be fixed under the governance of the BSC at a level that, to a first approximation, (a) allocated the heating element of the transmission system losses on an average basis, with little under or over recovery (heating variable losses), and (b) resulted in other transmission losses being allocated on a uniform basis (fixed losses) through the parameters TLM0. Any inaccuracy in (a) would be compensated for in (b). Separate Zonal TLFs will be calculated for both generation and demand. The zonal TLFs for each season would be published on the Elexon website at least one month prior to the applicable period. BSCCo will map BMUs to the applicable zones. This mapping would be published at least one month prior to the application of TLFs, made available to BSC parties in electronic format and be revised from time to time. The volume of transmission losses in each Settlement Period for the applicable period would be allocated amongst individual BMUs in settlement by applying the relevant zonal TLFs, TLMO+j and TLMO-j. In order to provide an opportunity for parties to prepare for the introduction of a zonal losses scheme, we propose an implementation date of April 2008. The scheme should be cost effective, not introduce unnecessary or untoward risks on parties and be simple to audit. |
| Description of Issue or Defect that Modification Proposal Seeks to Address (mandatory by originator) Under the current BSC arrangements all transmission system losses are allocated to BSC parties in proportion to metered energy, whether production or consumption on a uniform allocation basis (45% to production accounts, 55% to consumption accounts). Therefore, the cost of heating (variable) transmission losses is allocated amongst BSC Parties regardless of the extent to which they give rise to them. This means that customers in the north of GB and generators in the south of England have to pay some of the costs of transmitting electricity to locations miles away from the source of generation. The proposed seasonal zonal scheme will enable the variable costs of transmission losses to be allocated on a cost-reflective basis and reflected on parties that cause them. The modification would remove the current cross subsidies and associated discrimination that is inherent in the uniform allocation of transmission losses. The current allocation of transmission losses fails to provide potential connectees to the transmission system with appropriate signals regarding the implications of siting in different parts of the country. This may give rise to inefficient decisions regarding the development of new power stations or connection of new industrial loads. This results in the inefficient use of energy and unnecessary carbon emissions. A seasonal zonal transmission losses scheme would enable long-term locational signals for losses to be introduced into the GB electricity market. It is anticipated that to the extent that the seasonal zonal charging of losses influences the use of existing generation and the location of future investment, it will reduce the total amount of electricity transmitted and therefore increase the efficient use of energy. Earlier studies of a similar proposal have indicated that such a scheme could reduce carbon emissions in the short term by between 2000 tonnes p/a and 6000 tonnes p/a. These savings could increase to between 48,000 tonnes p/a and 127,000 tonnes p/a in the longer term. The modification would be based on work already completed on a seasonal alternative to P198 at the modification group but would not include any linear phasing. The work at the group has identified that there are additional benefits arising from a seasonal scheme when compared with an annual scheme in the form of the reduced overall cost of losses. |
| Impact on Code (optional by originator) |
| Impact on Core Industry Documents or System Operator-Transmission Owner Code (optional by originator) |
| Impact on BSC Systems and Other Relevant Systems and Processes Used by Parties (optional by originator) |
| Impact on other Configurable Items (optional by originator) |
| Justification for Proposed Modification with Reference to Applicable BSC Objectives (mandatory by originator) The proposal will better facilitate BSC Objective A relating to the efficient discharge by the licensee (NGC) of the obligations imposed upon it by its licence. A seasonal zonal transmission losses scheme will remove market distortions and the discrimination that exist in the present arrangements. The proposal will better facilitate BSC Objective B by enhancing the efficient, economic and co-ordinated operation by the licensee (NGC) of the licensees transmission system. Adoption of a seasonal zonal transmission losses scheme will remove cross subsidies which the present uniform charging for transmission losses create. A seasonal zonal transmission losses scheme will therefore enhance efficiency through more cost reflective charging which could be expected to influence both short term plant despatch and long term business decisions influencing investment in both generation and demand. In addition, cost benefit work during assessment of P198 has demonstrated that a seasonal zonal losses scheme is capable of delivering additional efficiency benefits in terms of reduced overall losses when compared to an annual losses scheme. This proposal will also contribute to better achieving the BSC objective C relating to the promotion of effective competition in the generation and supply of electricity, and (so far as consistent therewith) and the promotion of such competition in the sale and purchase of electricity. In particular: The proposal will introduce a cost reflective allocation of transmission losses according to the degree to which BMUs in an applicable zone give rise to losses; The proposal removes the current cross subsidies between customers (north to south) and generators (south to north) that occur through the uniform allocation of transmission losses; The allocation of losses to zones will enable the costs to be reflected on generation and demand in a manner that does not unduly penalise individual BMUs; A scheme based on the ex ante calculation of zonal loss factors will enable users of the transmission system to estimate the impact and appropriately reflect the costs; A seasonal zonal scheme would provide better information to users of the transmission system regarding the implications of siting generation and new load in different parts of the country; and In the longer term seasonal zonal allocation of transmission losses would encourage appropriate investment in generation or new load in areas which currently have limited capacity relative either to generation or demand. This will ultimately bring down the overall costs of losses with benefits for customers and the environment. |
| Details of Proposer: Name: Terry Ballard Organisation: RWE Npower Telephone Number: 07989 493038 Email Address: terry.ballard@rwenpower.com |
| Details of Proposer’s Representative: Name: Bill Reed Organisation: RWE Trading Telephone Number: 01793 893835 Email address: bill.reed@rwe.com |
| Details of Representative’s Alternate: Name: Terry Ballard Organisation: RWE Npower Telephone Number: 07989 493038 Email Address: terry.ballard@rwenpower.com |
| Attachments: Yes / No (delete as appropriate) (mandatory by originator) If Yes, Title and No. of Pages of Each Attachment: |

Appendix 2: Initial Assessment of Impacts of Modification Proposal

An initial assessment has been undertaken by BSCCo in respect of all BSC systems, documentation and processes.  The following have been identified as being potentially impacted by P203.

Please note that the impacts listed below are based on the assumption that (with the exception of the removal of the phasing element) the solution for Proposed Modification P203 will be identical to that developed for Alternative Modification P198.  Copies of the impact assessment responses received for Alternative Modification P198 can be found in the P198 Second Assessment Procedure Consultation Document.

Impact on BSC Systems and Processes

| System / Process | Impact of Proposed Modification |
| --- | --- |
| BM Unit Registration | The CRA would be required to amend its BM Unit registration process so that Adjusted Seasonal Zonal TLF values for each BM Unit are obtained from the TLFA (via BSCCo) for each BSC Year, and are registered in BSC Systems. These values would be reported using existing data flows. |
| Central Data Collection | The CDCA would be required to provide the TLFA (via BSCCo) with Metered Volume data for the Sample Settlement Periods used in the Load Flow Model. |
| BMRS | The BMRA would be required to receive Adjusted Seasonal Zonal TLF values for each BM Unit from the CRA, and to use these values in BMRA reporting during the applicable BSC Year. |
| Settlement Administration | The SAA would be required to receive Adjusted Seasonal Zonal TLF values for each BM Unit from the CRA, and to apply these values in Settlement calculations during the applicable BSC Year. |
| Derivation of Zonal TLFs | A new BSC process, with supporting systems, would be introduced for the TLFA to derive TLFs through the application of a Load Flow Model in accordance with a Network Mapping Statement, Load Flow Model Specification, and new calculations in Section T of the Code. The output of this new process would be a set of four Adjusted Seasonal Zonal TLF values (one per BSC Season in the year) for each of the 14 TLF Zones. All BM Units within a Zone would receive the Adjusted Seasonal Zonal TLF value for that Zone in the relevant BSC Season. |

All of the above processes would contain the flexibility to handle the following activities:

- Ad-hoc prospective registration of TLFs for new BM Units; and

- Ad-hoc retrospective recalculation of TLF values following an upheld Trading Dispute.

BSC Agent documentation (e.g. Interface Definition and Design, Design Specifications, System Specifications, Manual System Specifications and Operating System Manuals) would need to be amended/developed to reflect the changes outlined above.

Impact on BSC Agent Contractual Arrangements

| BSC Agent Contract | Impact of Proposed Modification |
| --- | --- |
| Transmission Loss Factor Agent | A full BSC Agent procurement exercise would need to be undertaken, and appropriate contractual arrangements created, for the TLFA in accordance with Section E of the Code. |
| BSC Auditor | The scope of the BSC Audit would need to be extended to include the new BSC Agent, the TLFA. |

Impact on BSC Parties and Party Agents

Parties may wish to verify the allocation of their BM Units to Zones.  Parties that have developed their own systems to monitor the Settlement calculations would also need to amend these to take account of the existence of non-zero TLF values which vary by BSC Season.

P203 has no impact on any Party Agents.

Impact on Transmission Company

P203 would have the following impact on the Transmission Company:

- The Transmission Company would be required to support BSCCo and the Panel in establishing and maintaining the Network Mapping Statement – including the maintenance of an up-to-date list of all Nodes on the Transmission System, and assistance in resolving any question or dispute over the allocation of individual BM Units to Zones; and

- The Transmission Company would be required to support the TLFA and the Panel in maintaining the Load Flow Model, including the provision of relevant Network Data and any necessary information to aid the Panel in its determination of Load Periods.

Impact on BSC Panel

P203 would have the following impact on the Panel:

- The Panel would be responsible for approving the Load Flow Model, the Load Flow Model Specification, the TLFA Service Description, the Load Flow Model Reviewer Terms of Reference and the Network Mapping Statement;

- The Panel would be responsible for establishing the definitive list of TLF Zones for use in the Network Mapping Statement and Load Flow Model, including the resolution of any question or dispute over the mapping of individual BM Units to Zones;

- The Panel would be responsible for establishing, for use in the Load Flow Model, a number of different Load Periods to represent varying levels of load on the Transmission System;

- The Panel would be responsible for establishing, for use in the Load Flow Model, the number of Sample Settlement Periods to be used in each Load Period;

- The Panel would be responsible for establishing a revised BSC Audit Scope incorporating the TLFA; and

- The Panel (aided by an independent Load Flow Model Reviewer) would be responsible for ensuring that the Load Flow Model complies with the Load Flow Model Specification – including retrospectively, where the calculation or use of TLFs is the subject of a Trading Dispute.

Impact on BSCCo

| Area of Business | Impact of Proposed Modification |
| --- | --- |
| BSC Website | BSCCo would be required to publish the following TLF data and documents on the BSC Website: The four Adjusted Seasonal Zonal TLF values for each TLF Zone in the applicable BSC Year; The version of the Network Mapping Statement used in the annual TLF calculation, and any subsequent amendments to that statement to take account of changes in BM Unit registrations; and The Load Periods and Sample Settlement Periods used in the TLF calculation for the applicable BSC Year. Any existing website references to TLF=0 would also need to be amended. |
| Communications | BSCCo would produce an information sheet for Parties explaining the new P198 process, for publication on the BSC Website. |
| Working Procedures | BSCCo would need to put in place appropriate working practices to support its Code obligations regarding the derivation and use of TLFs. These would include processes for requesting Node information and Network Data from the Transmission Company, requesting Metered Volume data from the CDCA, and allocating new BM Units to Zones. |
| BSC Panel/Panel Committee Support | BSCCo would be required to assist the Panel in its determination of TLF Zones, Load Periods and Sample Settlement Periods. BSCCo would be required to support the Panel in its determination of any question or dispute over the mapping of individual BM Units to TLF Zones (potentially including the development of appeal guidelines). BSCCo would be required to develop a revised methodology for ETLMO values to reflect zonal TLFs, and to support the ISG in its approval of that methodology. Any potential incorrect calculation or use of TLF values in Settlement would form the subject of a Trading Dispute, under the normal process administered by BSCCo on behalf of the TDC. BSCCo and TDC working practices regarding such Disputes would require additional steps for the TDC to decide whether to obtain a report from the Load Flow Model Reviewer on the compliance of the Load Flow Model with its specification, and for the Panel to determine whether TLFs should be recalculated. |
| Change and Configuration Management | BSCCo would be required to maintain the Network Mapping Statement on behalf of the Panel, under a specific change process to be detailed in the Code. |
| Procurement and Contract Management | BSCCo would be required to procure the TLFA and Load Flow Model Reviewer, and to manage the resulting contracts. BSCCo would also be required to manage the escrow arrangements for the Load Flow Model. |
| Performance Assurance | BSCCo would be required to provide any necessary additional support to the BSC Auditor and the Panel in extending the scope of the BSC Audit to incorporate the TLFA. |

Impact on Code

| Code Section | Impact of Proposed Modification |
| --- | --- |
| Section E ‘BSC Agents’ | The TLFA would need to be added to the list of existing BSC Agents in Section E. |
| Section H ‘General’ | The Load Flow Model Specification would need to be added to the list of Code Subsidiary Documents in Section H. |
| Section T ‘Settlement and Trading Charges’ | Section T would require amendments to detail the rights and obligations of all relevant parties regarding the derivation of Adjusted Seasonal Zonal TLFs and their use in Settlement. |
| Section V ‘Reporting’ | Section V would require amendment to detail the provision by BSCCo of the following TLF data to Parties on request: The Network Data and Metered Volumes used in the TLF calculation for the applicable BSC Year; and The raw nodal power flows calculated by the Load Flow Model and used in the TLF calculation for the applicable BSC Year; and The raw Nodal TLFs calculated by the Load Flow Model and used in the TLF calculation for the applicable BSC Year. |
| Section X ‘Definitions and Reporting’ | Section X would require amendment to detail any new Code-defined terms or acronyms required for P203. |

Impact on Code Subsidiary Documents

| Document | Impact of Proposed Modification |
| --- | --- |
| BSCP01 ‘Overview of the Trading Arrangements’ | Amendments would be required to reflect the derivation of non-zero TLFs and their use in Settlement calculations. |
| BSCP15 ‘BM Unit Registration’ | Amendments would be required to include the process for allocating four Adjusted Seasonal Zonal TLF values to each BM Unit in the applicable BSC Year. |
| BSCP38 ‘Authorisations’ | Amendments would be required to include an authorisation process for Parties to request input and output data files relating to the Load Flow Model (Network Data, Metered Volumes, power flows and Nodal TLFs). |
| BSCP41 ‘Report Requests and Authorisations’ | As above. |
| Reporting Catalogue | Amendments would be required to reflect the new/amended reporting requirements introduced by P198. |
| Communications Requirement Document | Amendments would be required to reflect the rules for communicating with the TLFA via BSCCo. |
| BSC Agent Service Descriptions | The BMRS, BSC Auditor, CDCA, CRA and SAA Service Descriptions would need to be amended to reflect the new obligations on these Agents in respect of zonal TLFs. A new Service Description would need to be developed for the TLFA. |
| Load Flow Model Specification | The specification for the TLFA Load Flow Model would be established as a new Code Subsidiary Document. |

Impact on Core Industry Documents/System Operator-Transmission Owner Code

No impact.

Impact on Other Configurable Items

| Document | Impact of Proposed Modification |
| --- | --- |
| User Requirements Specifications | The BMRS, BSC Website, CDCA, and CRA URSs would need to be amended to reflect the new obligations on these Agents in respect of zonal TLFs. A new URS would need to be developed for the TLFA. |

Impact on BSCCo Memorandum and Articles of Association

No impact.

Impact on Governance and Regulatory Framework

The P198 Modification Group agreed that the following potential impacts of P198 fell outside the vires of the Code, and could therefore not form part of its assessment against the Applicable BSC Objectives:

- Impact on the environment (through changes in carbon emissions, plant-mix, or the location of generation and demand);

- Impact on consumers (through the passing on of costs or cost-savings by Parties, or changes in the location of demand);

- Impact on the existing locational signals provided by the Transmission Company’s TNUoS charging.

The Group noted that these areas could be taken into account by the Authority as part of its wider statutory duties when making its decision whether to approve P198.  The same arguments are expected to apply to P203.

Appendix 3: Costs and Timetable for Progression

| ESTIMATED COSTS OF PROGRESSING MODIFICATION PROPOSAL |
| --- |
| Meeting Cost | £1,000 (based on sharing both meetings with P204) |
| Legal/Expert Cost | £0 |
| Impact Assessment Cost | £0 |
| ELEXON Resource | 15 man days £3,860 |

The gantt chart on the following page shows the proposed P203 timetable against the agreed/recommended timetables for P198, P200 and P204.

# Footnotes

ELEXON Ltd fulfils the role of the Balancing and Settlement Code Company (‘BSCCo’), pursuant to Annex X-1 of the Balancing and Settlement Code (the ‘Code’).

The current version of the Code can be found at http://www.elexon.co.uk/bscrelateddocs/BSC/default.aspx.

In practice, this is designed to be equivalent to a 50:50 allocation, but with allowance for the fact that metering for most generation connections is on the high voltage side of the supergrid transformer, whereas that for demand is on the low voltage side.  The 45:55 allocation of transmission losses is intended to allow for supergrid transformer losses for demand connections which are in addition to the metered flow.

Applicable BSC Objectives (a) ‘The efficient discharge by the Transmission Company of the obligations imposed upon it by the Transmission Licence’, (b) ‘The efficient, economic and co-ordinated operation of the GB transmission system’, and (c) ‘Promoting effective competition in the generation and supply of electricity, and (so far as consistent therewith) promoting such competition in the sale and purchase of electricity’.

Clarification of the meanings of the cost terms in this appendix can be found on the BSC Website at the following link:

http://www.elexon.co.uk/documents/Change_and_Implementation/Modifications_Process_-_Related_Documents/Clarification_of_Costs_in_Modification_Procedure_Reports.pdf

# Text boxes

*New document/role introduced by P203

116/05